## Slide 1: Unit 17 Design of Pressure Vessels
组长：唐健
汇报：邵寅 唐健 刘园园
罗志明 秦长久 王帅
PPT：刘小松 王佳鑫

## Slide 2: part 1
汇报人：邵寅

## Slide 3: Words and Expressions
1.installation [ˌɪnstəˈleɪʃn] n.安装，装置
2.earthquake [ˈɜːθkweɪk] n.地震
3.erection [ɪˈrekʃn] n.竖立，安装
4.petrochemical [ˌpetrəʊˈkemɪkl] a.山石油化工的
5.degradation [ˌdeɡrəˈdeɪʃn] n.降级，退化
6.substitution [ˌsʌbstɪ'tjuːʃ(ə)n] n.代替，取代
7.prevalent [ˈprevələnt] a.普遍的，流行的
8.integrity [ɪnˈteɡrəti] n.完整性
9.assembly [əˈsembli] n.组合，装配
10.assurance [əˈʃʊərəns] n.确信，保证，保险
11.adverse [ˈædvɜːs] a.不利的，有害的，敌对的
12.radiography [ˌreɪdiˈɒɡrəfi] n.射线照相，X光探伤

## Slide 4: Words and Expressions
13.encounter [ɪnˈkaʊntə(r)] v.遭遇，碰到
14.jurisdiction [ˌdʒʊərɪsˈdɪkʃn] n.权限，管辖权
15.erosion [ɪˈrəʊʒn] n.腐蚀，冲刷
16.lethal [ˈliːθl] a.致命的，致死的
17.sustained [səˈsteɪnd] a.持续的，不衰减的
18.transient [ˈtrænziənt] a.瞬态的，过渡的
19.assumption [əˈsʌmpʃn] n.假设，设想，前提
20.specification [ˌspesɪfɪˈkeɪʃn] n.技术要求，详细说明，说明书
21.certification [ˌsɜːtɪfɪˈkeɪʃn] n.证明，确认，鉴定
22.margin [ˈmɑːdʒɪn] n.差距，边界
23.mode [məʊd] n.形式，状态，振型
24.criterion [kraɪˈtɪəriən] n.判据，准则，指标（ pl. criteria)

## Slide 5: part 2
汇报人：秦长久

## Slide 6
正文：
Selection of Vessel Although many factors contribute to the selection of pressure vessels，the two basic requirements that affect the selection are safety and economics. Many items are considered，such as materials’ availability，corrosion resistance ， materials’ strength，types and magnitudes of loadings, location of installation including wind loading and earthquake loading，location off abrication
— (shop or field ) ， position of vessel installation ， and availability of labor supply at the erection site. With increasing use of special pressure vessels in the petrochemical and other industries, the availability of the proper materials is fast becoming a major problem. The most usual material for vessels is carbon steel. Many other specialized materials are also being used for corrosion resistance or the ability to contain a fluid without degradation of the material ’properties. Substitution of materials is prevalent and cladding and coatings are used extensively. The design engineer must be in communication with the process engineer in order that all materials used will contribute to the overall integrity of the vessel. For those vessels that require field assembly in contrast to those that can be built in the shop， proper quality assurance must be established for acceptable welding regardless of the adverse conditions under which the vessel is made. Previsions must be established for radiography，stress relieving and other operations required in the field.

## Slide 7
Selection of Vessel Although many factors contribute to the selection of pressure vessels，the two basic requirements that affect the selection are safety and economics.
容器的选择 尽管影响压力容器的因素很多，但最基本的两个要求是：安全和经济。

## Slide 8
Many items are considered，such as materials’availability，corrosion resistance ， materials’ strength，types and magnitudes of loadings, location of installation including wind loading and earthquake loading，location of fabrication — (shop or field ) ， position of vessel installation ， and availability of labor supply at the erection site.
许多因素要考虑，列如材料是否容易得到，腐蚀的控制，材料的强度，载荷的种类和控制，安装的状况，其中包括风载荷，雪载荷及地震载荷，制造地点是在车间还是在现场进行组装，还有在设备使用地点雇佣劳动工人是不是方便。
shop 车间（机械工程）
field 旷野，战场

## Slide 9
With increasing use of special pressure vessels
  in the petrochemical and other industries, the availability of the proper materials is fast becoming a major problem. The most usual material for vessels is carbon steel.
在石油化工还有其他工业中，随着特殊压力容器的越来越广泛的使用，合适材料是否容易得到这一问题日益突出。压力容器最常用的的材料是碳钢。

## Slide 10
Many other specialized materials are also being used for corrosion resistance or the ability to contain a fluid without degradation of the material ’properties. Substitution of materials is prevalent and cladding and coatings are used extensively.
许多特殊材料被用来控制腐蚀及不破坏所盛装物料的特性。材料的替代品现在逐渐流行起来，材料的覆层及涂层现在也被广泛的应用

## Slide 11
The design engineer must be in communication with the process engineer in order that all materials used will contribute to the overall integrity of the vessel.
设计工程师必须与过程工程师进行交流来保证所有使用的材料都有助于容器整体的完整性。

## Slide 12
For those vessels that require field assembly in contrast to those that can be built in the shop， proper quality assurance must be established for acceptable welding regardless of the adverse conditions under which the vessel is made. Previsions must be established for radiography，stress relieving and other operations required in the field.
与能在车间生产的设备相比，对需在现场进行安装的设备，为了避免制造过程中有害因素的影响，对焊接必须建立合理的安全技术保证。对射线探伤，缓解应力，还有该领域的其他操作，必须建立相应的规范。

## Slide 13: part 3
汇报人：唐健

## Slide 14
正文：
For those vessels that will operate in climates where low temperatures are encountered or contain fluids operating at low temperatures, special care must be taken to ensure impact resistance of the materials at low temperatures ① .To obtain this property, the vessel may require a special high-alloy steel, nonferrous material, or some special heat treatment.
Which Pressure Vessel Code Is Used The first consideration must be whether or not there is a pressure vessel law at the location of the installation. If there is, the applicable codes are stated in the law. If the jurisdiction has adopted the ASME Code, Section Ⅷ , the decision may be narrowed down to selecting whether Division 1 or Division 2 is used .
There are many opinions regarding the use of Division 1 versus Division 2, but the“ botto line ”is economics.Division 1 uses approximate formulas ， charts， and graphs in simple calculations. Division 2， on the other hand,uses a complex method of formulas,charts, and design-by-analysis which must be described in a stress report. Sometimes so many additional requirements are added to the minimum specifications of a Division 1 vessel that it might be more economical to supply a Division 2 vessel and take advantage of the higher allowable stresses .

## Slide 15
For those vessels that will operate in climates where low temperatures are encountered or contain fluids operating at low temperatures, special care must be taken to ensure impact resistance of the materials at low temperatures.
对于那些在低温环境下运行或盛装低温流体的容器，必须特别注意保证材料在低温下的抗冲击能力。

## Slide 16
To obtain this property, the vessel may require a special high-alloy steel, nonferrous material, or some special heat treatment.
为保证这一特性，压力容器可能需要高合金钢，有色金属材料，或进行一些特殊热处理

## Slide 17
Which Pressure Vessel Code Is Used The first consideration must be whether or not there is a pressure vessel law at the location of the installation.
应用哪种压力容器规范 首先要考虑的是在安装地是否有压力容器方面的相关法规。

## Slide 18
If there is, the applicable codes are stated in the law. If the jurisdiction has adopted the ASME Code, Section Ⅷ , the decision may be narrowed down to selecting whether Division 1 or Division 2 is used.
如果有，在法规中有相应的规定，如果管辖部门已经决定采用ASME规范中的第Ⅷ篇，那未需要确定的只是选用第一篇还是第二篇。

## Slide 19
There are many opinions regarding the use of Division 1 versus Division 2, but the“ botto line”is economics.Division 1 uses approximate formulas，
charts， and graphs in simple calculations.
关于第一篇和第二篇的应用，有许多的选择性。第一篇应用许多近似的公式，表格和图表来进行简单的计算。

## Slide 20
Division 2，on the other hand,uses a complex method of formulas,charts, and design-by-analysis which must be described in a stress report.
第二篇应用复杂的方法，表格和必须在压力容器中表述的分析设计。

## Slide 21
Sometimes so many additional requirements are added to the minimum specifications of a Division 1 vessel that it might be more economical to supply a Division 2 vessel and take advantage of the higher allowable stresses.
有时由于对按第一篇设计的容器在最低要求之外有增加了许多附加要求，应此按第二篇设计并选取许用应力可能更为经济。

## Slide 22: part 4
汇报人：罗志明

## Slide 23
正文：
Special Design Requirements In addition to the standard information required on all units，such as design pressure，design temperature，geometry，and size，many other items of information are necessary and must be recorded. The corrosion and erosion amounts are to be given and a suitable material and method of protection are to be noted. The type of fluid that will be contained, such as lethal，must be noted because of the required specific design details. Supported position, vertical or horizontal, and support locations must be listed as well as any local loads from supported equipment and piping. Site location is given so that wind, snow，and earthquake requirements can be determined. Impact loads and cyclic requirements are also included.
For the ASME Code，Ⅷ-2，a statement as to whether or not a fatigue analysis is required according to AD-160 is given. If a fatigue analysis is required，the specific cycles and loadings will be given. In addition, the design specifications state whether or not certain loadings are sustained or transient. The allowable stresses vary with the type of loadings.

## Slide 24
Special Design Requirements In addition to the standard information required on all units，such as design pressure，design temperature，geometry，and size，many other items of information are necessary and must be recorded.
特殊的设计要求 此外，标准的数据需要包含所有装置的参数，比如设计压力、设计温度、几何形状以及尺寸，许多其他项目的信息也是必要的并且必须被记录下来。

## Slide 25
The corrosion and erosion amounts are to be given and a suitable material and method of protection are to be noted. The type of fluid that will be contained, such as lethal，must be noted because of the required specific design details.
腐蚀和磨损量要被给出，合适的材料和保养方法也要注意。
由于需要特殊的设计细节，将来要承装液体的类型必须注意，比如有害的。

## Slide 26
Supported position, vertical or horizontal, and support locations must be listed as well as any local loads from supported equipment and piping.
Site location is given so that wind, snow，and earthquake requirements can be determined. Impact loads and cyclic requirements are also included.
支撑方位是水平还是竖直、支撑的位置以及来自支撑设备和管子的局部载荷都要被列出。
坐落的位置也要给出，这样风、雪、地震的要求也能够得到确定。冲击载荷和循环载荷的要求也要被包括。

## Slide 27
For the ASME Code，Ⅷ-2，a statement as to whether or not a fatigue analysis is required according to AD-160 is given. If a fatigue analysis is required，the specific cycles and loadings will be given.
由ASME标准第八篇第二分册，是否需要做疲劳分析的说明已经通过AD-160给出。如果需要做一个疲劳分析，那么一个特殊的循环载荷就会被给出。

## Slide 28
In addition, the design specifications state whether or not certain loadings are sustained or transient. The allowable stresses vary with the type of loadings.
另外，设计说明书会指出是否某一载荷是恒定的还是瞬时的。许用应力随着载荷种类而变化。

## Slide 29: part 5
汇报人：刘园园

## Slide 30
正文：
Design Reports and Calculations The ASME Code，Ⅷ-2,requires a formal design report with the assumptions in the User’s Design Specification incorporated in the stress analysis calculations. These calculations are prepared and certified by a registered professional engineer experienced in pressure vessel design. As with the User ’ s Design Specification，the Manufacturer’s Design Report is mandatory and the certification reported on the Manufacturer’s Data Report®. This is kept on file by the manufacturer for five year.
Materials’ Specifications All codes and standards have materials' specifications and requirements describing what materials are permissible. Those materials that are permitted with a specific code are either listed or limited to the ones that have allowable stress values given. Depending upon the code or standard, permitted materials for a particular process vessel are limited. For instance, only materials with an SA or SB designation can be used in ASME Boiler and Pressure Vessel Code construction.

## Slide 31
Design Reports and Calculations The ASME Code，Ⅷ-2,requires a formal design report with the assumptions in the User’s Design Specification incorporated in the stress analysis calculations.
These calculations are prepared and certified by a registered professional engineer experienced in pressure vessel design.
设计报告与计算 ASME VIII-2需要一个正式的设计报告，其中包含使用者的设计技术要求并伴有应力分析计算。
这些计算由一个在压力容器设计方面很有经验的专业注册工程师制定并验证。

## Slide 32
As with the User ’s Design Specification，the Manufacturer’s Design Report is mandatory and the certification reported on the Manufacturer’s Data Report®. This is kept on file by the manufacturer for five year.
如同用户的设计技术要求一样，制造商的设计报告以及有关制造商数据报告的证明书都是强制性的。这要被制造商记录为文件并保存五年。

## Slide 33
Materials’Specifications All codes and standards have materials' specifications and requirements describing what materials are permissible. Those materials that are permitted with a specific code are either listed or limited to the ones that have allowable stress values given.
材料的确定 所有的规范和标准都包含材料的确定与要求，用来描述哪些材料是被允许的。这些获得特殊标准许可的材料要么被列出，要么被限制的用于给定许用应力值的场合。

## Slide 34
Depending upon the code or standard, permitted materials for a particular process vessel are limited. For instance, only materials with an SA or SB designation can be used in ASME Boiler and Pressure Vessel Code construction.
根据规范和标准，一个特殊的压力容器其许用材料是被限制的。例如，只有拥有SA与SB标识的材料可以用于ASME锅炉和压力容器的制造中。

## Slide 35: part 6
汇报人：王帅

## Slide 36
正文：
Factors of Safety In order to provide a margin of safety between exact formulas，which are based on complex theories and various modes of failure, and the actual design formulas used for setting the minimum required thicknesses and the stress levels, a factor of safety (FS) is applied to various materials’ properties that are used to set the allowable stress values. The factors of safety are directly related to the theories and modes of failure, the specific design criteria of each code, and the extent to which various levels of actual stresses are determined and evaluated.
Throughout the world, various factors of safety are applied to materials' data to establish allowable stresses for the design of boilers, pressure vessels, and piping. For the temperature range to that temperature where creep or rupture sets the allowable stresses，the universal factor for setting allowable stresses is based on yield strength. In some countries, a factor is applied to sets of data that have been established from many tests； in others，the data are determined by the low yield point or the high yield point. In still other countries，the actual data for the component being designed have its yield strength determined by tests. The actual data of the part are then factored into the design formulas. Not all countries choose to use the ultimate tensile strength as a criterion for setting allowable stresses.

## Slide 37
Factors of Safety In order to provide a margin of safety between exact formulas，which are based on complex theories and various modes of failure, and the actual design formulas used for setting the minimum required thicknesses and the stress levels, a factor of safety (FS) is applied to various materials’ properties that are used to set the allowable stress values.
安全因素 为了提供一个在精确公式与实际设计公式间的安全界限，一个安全因素（FS）被用在确定各种材料许用应力值的性能上。其中精确公式基于复杂的理论与大量失效模型，而实际的设计公式用于确定最小需要壁厚与应力等级。

## Slide 38
The factors of safety are directly related to the theories and modes of failure, the specific design criteria of each code, and the extent to which various levels of actual stresses are determined and evaluated.
安全因素直接涉及理论、失效模型、各标准中的特殊设计准则，还有已经被评估确定的各种实际应力等级的程度。

## Slide 39
Throughout the world, various factors of safety are applied to materials' data to establish allowable stresses for the design of boilers, pressure vessels, and piping.
纵观世界，各种安全因素被用在材料的数据上，以此建立在设计锅炉、压力容器和管子时的许用应力。

## Slide 40
For the temperature range to that temperature where creep or rupture sets the allowable stresses，the universal factor for setting allowable stresses is based on yield strength.
从温度范围来看，蠕变或断裂温度确定了许用应力，但建立许用应力所通用的因素却是基于屈服强度的。

## Slide 41
In some countries, a factor is applied to sets of data that have been established from many tests； in others，the data are determined by the low yield point or the high yield point.
In still other countries，the actual data for the component being designed have its yield strength determined by tests.
在一些国家，由多次试验确认过的因素被用于数据的建立。
在另一些国家，这些数据则是由最低屈服点或最高屈服点决定。
在其他另外的国家，被设计分量的实际数据是根据测试来确定
其屈服强度的。

## Slide 42
The actual data of the part are then factored into the design formulas. Not all countries choose to use the ultimate tensile strength as a criterion for setting allowable stresses.
然后，部分的实际数据被写入设计公式。并不是所有国家都使用极限抗拉强度来作为确定许用应力的准则。

## Slide 43
The end